- Font conversion tool from FTDI: v0.4
- Used font Tuffy.ttf. Provided by FTDI with the conversion tool.
- When used ansi text file, used file provided by FTDI with conversion tool (ANSI_32_126.txt)

***********************************************************

For all options: (for RAM_G offset 0, so, address = 0)
- Tool generates an array of data.
- First 148 bytes are the metrics block.
- Then, for all options, tool generates font raw data with length = 8265 bytes.
- So total lenght of array = 8265 + 148 = 8413
- Allways generates data for 95 characters.
- It looks that generated raw data is allways the same (verified with winmerge.exe).
- Then. Changes only in header block?
- In header: format, stride, maxwidth, maxheight is allways the same. So it looks that there are changes only in widths and raw data address.
**********************************************************
layout = L1
stride = 3
max width = 20
max height = 29

byte per font = stride * maxheight = 3 * 29 = 87

#if defined SETFONT
-------------------
Command Line:
fnt_cvt.exe -i Tuffy.ttf -s 24 -u ANSI_32_126.txt -c setfont

Widths (data for 95 characters):
0,7,4,9,19,12,16,14,5,7,6,12,11,5,10,5,11,13,13,13,14,13,13,14,13,13,14,5,5,10,11,10,12,20,15,13,14,14,13,13,16,14,5,13,15,13,18,14,16,13,16,13,12,15,14,15,18,14,14,16,8,12,8,11,15,6,11,13,11,12,12,9,12,13,5,7,12,6,19,13,12,13,13,10,11,8,12,12,16,11,12,12,8,4,9,9,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,

Raw data address in decimal: 61
61,0,0,0,

Results:
DLBitmapSource CMDSetfont2 *

61 (from array) 0 BAD.
61 (from array) 32 BAD. (numbers ok?)
148 (personal) 32 BAD. (first vertex & numbers ok?)
148 (personal) 0 BAD.

#if defined SETFONT_2
---------------------
Command Line:
fnt_cvt.exe -i Tuffy.ttf -s 24 -u ANSI_32_126.txt -c setfont2

Widths (data for 95 characters):
0,7,4,9,19,12,16,14,5,7,6,12,11,5,10,5,11,13,13,13,14,13,13,14,13,13,14,5,5,10,11,10,12,20,15,13,14,14,13,13,16,14,5,13,15,13,18,14,16,13,16,13,12,15,14,15,18,14,14,16,8,12,8,11,15,6,11,13,11,12,12,9,12,13,5,7,12,6,19,13,12,13,13,10,11,8,12,12,16,11,12,12,8,4,9,9,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,

Raw data address in decimal: 148
148,0,0,0,

Results:
DLBitmapSource CMDSetfont2 *

148 (from array) 0 BAD. vertex ok.
148 (from array) 32 BAD. (doesn´t looks good).

#if defined SETFONT_NOTEXT
--------------------------
Command Line:
Command Line: fnt_cvt.exe -i Tuffy.ttf -s 24 -a -c setfont

Widths (data for 95 characters):
0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,7,4,9,19,12,16,14,5,7,6,12,11,5,10,5,11,13,13,13,14,13,13,14,13,13,14,5,5,10,11,10,12,20,15,13,14,14,13,13,16,14,5,13,15,13,18,14,16,13,16,13,12,15,14,15,18,14,14,16,8,12,8,11,15,6,11,13,11,12,12,9,12,13,5,7,12,6,19,13,12,13,13,10,11,8,12,12,16,11,12,12,8,4,9,9,0,

Raw data address in decimal: -2636
180,245,255,255,

Results:
DLBitmapSource CMDSetfont2 *

148 (personal) 32 BAD.
148 (personal) 0 OK (second vertex bad, as expected)
-2636 (from array) 0 Vertex bad. Text & numbers ok.
        Display full of garbage.
-2636 (from array) 32 BAD.
        Display full of garbage.

2636 / (stride * maxheight) = 2636 / (3 * 29) = 30 (something here???)

#if defined SETFONT2_NOTEXT
---------------------------
Command Line:
Command Line: fnt_cvt.exe -i Tuffy.ttf -s 24 -a -c setfont2

Widths (data for 95 characters):
0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,0,7,4,9,19,12,16,14,5,7,6,12,11,5,10,5,11,13,13,13,14,13,13,14,13,13,14,5,5,10,11,10,12,20,15,13,14,14,13,13,16,14,5,13,15,13,18,14,16,13,16,13,12,15,14,15,18,14,14,16,8,12,8,11,15,6,11,13,11,12,12,9,12,13,5,7,12,6,19,13,12,13,13,10,11,8,12,12,16,11,12,12,8,4,9,9,0,

Raw data address in decimal: 148
148,0,0,0,

Results:
DLBitmapSource CMDSetfont2 *

148 (from array) 0 BAD. vertex ok.
148 (from array) 32 OK (second vertex bad, as expected)

++++++:

in code.

Test 1.
- first vertex (block 3), cell = 33, it shows char ‘A’ = index 65
- second vertex (block 5), cell = 33, it shows char ‘!’ = index 33

Test 2.
- first vertex (block 3), cell = 35, it shows char ‘C’ = index 67
- second vertex (block 5), cell = 35, it shows char ‘#’ = index 35

it looks that cmdsetfont2 offsets address (cell), it makes cell = index.
***** Generated by conversion tool. *****
***** When using ansi text file *****

95 characters are converted

Character:	Index No.

1
!	2
"	3
#	4
$	5
%	6
&	7
'	8
(	9
)	10
*	11
+	12
,	13
-	14
.	15
/	16
0	17
1	18
2	19
3	20
4	21
5	22
6	23
7	24
8	25
9	26
:	27
;	28
<	29
=	30
>	31
?	32
@	33
A	34
B	35
C	36
D	37
E	38
F	39
G	40
H	41
I	42
J	43
K	44
L	45
M	46
N	47
O	48
P	49
Q	50
R	51
S	52
T	53
U	54
V	55
W	56
X	57
Y	58
Z	59
[	60
\	61
]	62
^	63
_	64
`	65
a	66
b	67
c	68
d	69
e	70
f	71
g	72
h	73
i	74
j	75
k	76
l	77
m	78
n	79
o	80
p	81
q	82
r	83
s	84
t	85
u	86
v	87
w	88
x	89
y	90
z	91
{	92
|	93
}	94
~	95
***** Generated by conversion tool. *****
***** When not using ansi text file (option -a used *****

95 characters are converted

Character:	Index No.

32
!	33
"	34
#	35
$	36
%	37
&	38
'	39
(	40
)	41
*	42
+	43
,	44
-	45
.	46
/	47
0	48
1	49
2	50
3	51
4	52
5	53
6	54
7	55
8	56
9	57
:	58
;	59
<	60
=	61
>	62
?	63
@	64
A	65
B	66
C	67
D	68
E	69
F	70
G	71
H	72
I	73
J	74
K	75
L	76
M	77
N	78
O	79
P	80
Q	81
R	82
S	83
T	84
U	85
V	86
W	87
X	88
Y	89
Z	90
[	91
\	92
]	93
^	94
_	95
`	96
a	97
b	98
c	99
d	100
e	101
f	102
g	103
h	104
i	105
j	106
k	107
l	108
m	109
n	110
o	111
p	112
q	113
r	114
s	115
t	116
u	117
v	118
w	119
x	120
y	121
z	122
{	123
|	124
}	125
~	126